Issue: Speed up irregular programs

current unique solution:
- Out-of-order super scalar processors only.
  - Pros
    - solve the speed up problem
  - cons
    - poor power efficiency

How to specify register operands
by register name (RISC-V)
  - pros
  - cons
    - poor power efficiency, due to register renaming.
    - preventing an increase in the front-end width.
by inter-instruction distance (STRAIGHT)
  - pros
    - eliminates register renaming
  - cons
    - large increase in number of instructions, due to strong constraint in instruction placement

the paper review these two existing instruction set architectures (ISA)
Conventional RISC-V
STRAIGHT
then, propose novel solution and compare its performance with the existing ones
clock-hands
Clock-hands characteristics
- pros
  - does not require register renaming
  - reduce set of instruction (Risc-V like), due to looser constraints on instruction placement compared to STRAIGHT
- cons
  - a
Methodology
implemented cycle-accurate simulator,
implemented FPGA implementation
first-step compiler for Clockhands
valuated benchmarks including SPEC CPU

conclusion/remarks
On a machine with an eight-fetch width:
  1. results showed that Clock-hands consumes 7.4% less energy than RISC.
  1. performance was comparable to RISC.
simulating a futuristic up-scaled processor with a 16-fetch width.
  1. results showed that Clock-hands energy reduction increases up to 24.4%.
  1. which shows that Clock-hands enables a wider front-end.

Abstract

Introduction
existing operand specification
  1. convectional RISC-V architectures
  1. STRAIGHT Architecture
clock hand overview
  1. motivation and key Idea
  1. ISA Overview
  1. Advantages
clock-hands ISA
  1. appropriate numbers of hands
  1. Handling stack pointer
  1. Usage of hands
  1. Calling conventions
  1. Architectural state
Micro-architecture
  1. Register Pointer (RP) calculation stage
  1. Recovery mechanism
  1. Simultaneous multi-threading
clock-hands compiler
  1. compilation flow for clockhands
  1. hand Assignment algorithm
  1. Advance Register Assignment
Evaluation
  1. Methodology
  1. Results
Related work
conclusion

Paper outline
Each paper review should have four components:
summary (25%)
  1. What is the problem the paper tries to solve?
  1. What are the main ideas or insights of the paper?
strengths (25%)
  1. Does the paper solve the suggested problem well?
weakness (25%): not from that author already exposed
  1. You have to think critically and figure out if there is anything the paper did not address well.
Others (25%)
  1. Is there room for improvement? In other words, can you do better?
  1. What have you learned and what were your likes and dislikes in the paper?
  1. Your review may not exceed two pages, with a font size of 11-point and margins no smaller than 1 inch on all sides.
  1. Figures/tables are not allowed in the review.
  1. The submission should be a single file in .pdf or .docx (or .doc)

Paper errors
in the abstract section the paper first states the following “a recently proposed architecture called STRAIGHT specifies operands by inter-instruction distance, thereby eliminating register renaming”. Then a paragraph after they state “Clockhands does not require register renaming as in STRAIGHT” which is a contradiction, I think they meant to say RISC-V.

Draft
Clockhands: Rename-free Instruction Set Architecture for	Luis D. Pena
Out-of-order Processors	EECE.5821
# Summary
## What is the problem the paper tries to solve?
The paper address the problem of speeding up irregular programs while improving power efficiency. Irregular programs are key in the execution, optimization, and compilation of interpreted and high level programming languages, gaming,and social network analysis, to name a few applications. According to the paper, the only solution that the industry offer to speed up these processes is to integrate more massive out of order cores, which improve processor’s single thread performace, which is key to reduce latency. However, although this unique solution seems to solve the problem, it does so with a poor power efficiency.
## What are the main ideas or insights of the paper?
The paper tries to solve the problematic with a different approach, abandoning the idea of increasing out of order cores and focusing his attention in the ISA, and how existing instruction set architectures (ISA) manage register operads and how these affect power efficiency. Specifically, the paper reviews two existing ISAs, Conventional RISC-V, and STRAIGHT. The paper point out that RISC-V, specify register operands by register name. Due to register renaming poor power efficiecy emerge, preventing an increase in the front-end width. On the other hand, STRAIGHT manage register operads by inter-instruction distace, which eliminates register renaming, but due to its strong contraint in instruction placement, a large increase in number of instrunction is generated, which do not help with power efficiency either, since more instructions implies consuming more power.
The paper then propose a novel solution called Clockhands, and compare its power efficiency with RISCV and STRAIGHT. ClockHands try to take the good of both worlds, since as opose to RISCV it does not require register renaming, and in contrast to STRAIGHT it has looser constraints on instruction placement which reduce number of instruction generated at levels similar to RISCV.
# Strengths
## Does the paper solve the suggested problem well?
Methodology wise, the paper did a good job measuring each ISA against a common ruler or bechmarks including SPEC CPU 2006/2017. for this purpose, Implementing cycle-accurate simulator, FPGA implementation, and first-step compiler for Clockhands was necessary. This effort also allowed instruction count comparison of STRAIGHT and Clockhands which provided an empiric evidence of the cause of incresed instruction count in STRAIGHT, and a method of verification that this issue does not occur in Clockhands, but in the contrary that is similar to RISCV in terms of instruction counts, which is good since fewer instructions count improve power consuption.

The solution presented Clockhands, simulation was fundamental, to stimate power consumption. Overall, Clockhands did what it promised, reduce power consumption. Results presented show the following remarks:
On a machine with an eight-fetch width:
  1. results showed that Clock-hands consumes 7.4% less energy than RISC.
  1. And its performance was comparable to RISC.
simulating a futuristic up-scaled processor with a 16-fetch width.
  1. results showed that Clock-hands energy reduction increases up to 24.4%.
  1. which shows that Clock-hands enables a more power efficient and wider front-end
# Weakness
Although, they offer cycle-accurate simulation I think would’ve been beneficial to inlude different simulations. Simulation will always be that, a simulation, and although it can predits the trends it can never mimic reality, that is why having multiple methods to validate a proposed architecture is always welcome and simply good practice.
Also, taking in consideration that each ISA is unique and performe differently it would’ve been good to compare Clockhands with othes ISA besides RISC and STRAIGHT, since Clockhands took their strenghth and build upon them implementing a solution which didn’t includes their weaknesses.
I think there is room for improvement there.
## What have you learned and what were your likes and dislikes in the paper?
Although we covered the topic of how the different variables affect performance, CPI, ISA, etc. in class, it was refreshing to see in practice how the ISA can affect performace, spefically power consuption. Also, I liked also that I could relate with the terminolgy, and that the terms and concepts that we convered in class were relevant to undestand the paper. In addition, Im taking Advance digital design class in which we are introduce FPGA design, which I’m very exited about, and it was good to see that this paper used FPGA in the problematic of solving Computer architecture problematic, whih is a plus.
Overall, I didn’t have major dislikes,the paper was well written, however it was a little be confusing at first, since in the abstract section the paper first states the following “a recently proposed architecture called STRAIGHT specifies operands by inter-instruction distance, thereby eliminating register renaming”. Then a paragraph after they state “Clockhands does not require register renaming as in STRAIGHT” which is a contradiction, or maybe a bad choice of words, I think they meant to say Clockhands does not require register renaming like RISCV does, this idea was later clarified as we read the paper.